Code Listings

Main.c

#include <ME218_C32.h>

#include <stdio.h>

#include <timers12.h>

#include "Event_Stages.h"

void main(void)

{

//initialize the bowling game

Initialize_Game();

//Event detection loop: repeat forever

while (1)

{

Event_Stages();

}

}

Event_Stages.h

void Event_Stages(void);

void Initialize_Game(void);

void pause(unsigned int miliseconds);

char State_change(unsigned char prev_state, unsigned char current_state);

void Test(void);

void Reset_Game(void);

void Reset_Score(void);

void Decrease_Num_Tries(void);

void Increase_Score(void);

Event_Stages.c

#include <ME218_C32.h>

#include <stdio.h>

#include <timers12.h>

#include "LED_Controller.h"

#include "Utility.h"

#include "Pre_Start.h"

#include "Penny_Sensor.h"

#include "Count_Release.h"

#include "Get_Impact.h"

#include "Prize_Dispense.h"

#include "Score_Controller.h"

#include "Timer_Controller.h"

#include "Event_Stages.h"

#define PENNY_INSERT 1

#define PRE_START 2

#define COUNT_RELEASE 3

#define GET_IMPACT 4

#define PRIZE_DISPENSE 5

//game variables for this module:

static char stage = PENNY_INSERT;

static char difficulty = 1;

static int score = 0;

static char target = 0;

static char num_tries = 3;

void Initialize_Game(void)

{

//initialize the timer

TMRS12_Init(TMRS12_RATE_1MS);

//initialize the PreStart Module

Initialize_PreStart();

//initialize penny sensor module

Initialize_PennyInsert();

//initialize count release module

Initialize_CountRelease();

//initialize the get impact module

Initialize_Impact();

//initialize score controller

Initialize_Score();

//initialize time controller

Initialize_Timer();

//initialize prize dispenser

Initialize_Prize();

//clear all of the LEDs

Initialize_LEDs();

}

void Reset_Game(void)

{

//rest the number of tries to 3

num_tries = 3;

//indicate the new number of tries on the LEDs

Light_Num_Tries(num_tries);

}

void Reset_Score(void)

{

//set the score to be zero

score = 0;

//clear the score 7-segment LEDs

Clear_Score();

}

void Decrease_Num_Tries(void)

{

//subtract one try

num_tries -= 1;

//display the new number of tries

Light_Num_Tries(num_tries);

}

void Increase_Score(void)

{

//display the new score

Pulse_Score(Get_Last_Score());

//increase the score variable

score += Get_Last_Score();

}

void Event_Stages(void)

{

char x;

//detect which stage the game is currently in

switch(stage)

{

case PENNY_INSERT:

//sense the insertion of the penny

if (Penny_Insert() == 1)

{

//reset the score if it is the first try

if (num_tries == 3)

Reset_Score();

stage = PRE_START;

}

break;

case PRE_START:

//read the difficulty

difficulty = Get_Difficulty();

//see if the start button was pressed

if (Start_Press() == 1)

{

//select the appropriate target

target = Select_Target();

stage = COUNT_RELEASE;

}

break;

case COUNT_RELEASE:

//wait for the aiming countdown to expire

if (Countdown_Release(difficulty) == 1)

{

stage = GET_IMPACT;

}

break;

case GET_IMPACT:

//detect an impact event (miss or hit)

if (Get_Impact(difficulty, target) == 1)

{

//adjust the score and number of tries

Increase_Score();

Decrease_Num_Tries();

stage = PRIZE_DISPENSE;

}

break;

case PRIZE_DISPENSE:

//dispense prize or return to the penny insertion stage

x = Prize_Dispense(num_tries, score);

if (x == 1) //it is not yet time to dispense the prize

{

stage = PENNY_INSERT;

}

else if (x == 2) //the prize was dispensed

{

//reset the game

Reset_Game();

stage = PENNY_INSERT;

}

break;

}

}

Count_Release.h

void Initialize_CountRelease(void);

char Countdown_Release(char difficulty);

Count_Release.c

#include <ME218_C32.h>

#include <stdio.h>

#include <timers12.h>

#include "Utility.h"

#include "Timer_Controller.h"

#include "Count_Release.h"

void Initialize_CountRelease(void)

{

//initialize solenoid to be off

PTAD &= BIT5LO;

}

char Countdown_Release(char difficulty)

{

//return 0 to remain on this stage; 1 to move to next stage

static int countdown_timer = 0;

static unsigned int prev_time = 0;

static short flag = 1;

unsigned int current_time;

//get the current time

current_time = TMRS12_GetTime();

//if this is the first iteration

if(flag)

{

//set the previous time equal to the current time

prev_time = current_time;

//reset the countdown timer

countdown_timer = difficulty*1000;

//reset the flag

flag = 0;

}

//decrement the countdown timer

countdown_timer -= (current_time - prev_time);

//set the previous time equal to the current time

prev_time = current_time;

if (countdown_timer > 0)

{

//display the time on the timer

Set_Timer((char)(1+(countdown_timer)/1000));

return 0;

}

else

{

//clear the timer

Clear_Timer();

//activate the solenoid

PTAD |= BIT5HI;

//leave enough time for the penny to escape

pause(500);

//de-activate the solenoid

PTAD &= BIT5LO;

//set the flag back to one

flag = 1;

return 1;

}

}

Get_Impact.h

void Initialize_Impact(void);

char Get_Impact(char difficulty, char target);

char Select_Target(void);

int Get_Last_Score(void);

void Activate_Buzzer(void);

Get_Impact.c

#include <ME218_C32.h>

#include <stdlib.h>

#include <stdio.h>

#include <timers12.h>

#include <math.h>

#include "Utility.h"

#include "LED_Controller.h"

#include "Score_Controller.h"

#include "Get_Impact.h"

//module variable

static int score_add = 0;

void Initialize_Impact(void)

{

//set the entire T port as an input

DDRT = 0x00;

//initialize the buzzer to be off

PTAD &= BIT6LO;

}

char Select_Target(void)

{

int random;

//select a random pin between 0 and 7

random = TMRS12_GetTime()%8;

//random = TMRS12_GetTime()%2 + 6;

//clear all LEDs

Pin_LEDs_Off();

//turn the appropriate LED on

LED_On((char)random);

return (char)random;

}

char Get_Impact(char difficulty, char target)

{

static short flag = 1;

static unsigned int release_time = 0;

static unsigned int roll_time = 1400;

unsigned int current_time;

short i, j;

unsigned char bit = 0x00;

//if this is the first iteration

if(flag)

{

//set the initial release time

release_time = TMRS12_GetTime();

//set the flag such that it is no longer the first //iteration

flag = 0;

score_add = 0;

return 0;

}

//get the current time

current_time = TMRS12_GetTime();

//see if the timer has expired

if (current_time - release_time >= roll_time)

{

//the player missed pin since maximum roll time has expired

//turn the target LED off

LED_Off(target);

//indicate a MISS

LED_On(8);

//activate the buzzer

Activate_Buzzer();

//reset the first iteration flag

flag = 1;

score_add = 0;

return 1;

}

//check all of the switches to detect an impact

for (i=0; i <=7; i++)

{

int x;

//clear the test bit

bit = 1;

//set the test bit to 2^i

for (x=0;x<i;x++)

{

bit *= 2;

}

//see if the switch has been activated

if (PTT & bit)

{

//the switch has NOT been activated

}

else //the switch HAS been activated

{

//check if the correct switch was hit

if (i == target)

{

//the correct switch was hit, so increment the score

//turn the target LED off

LED_Off(target);

//indicate a HIT

LED_On(9);

//increment score according to the difficulty level

score_add = 300 - (difficulty-1)*50;

//flash the target LED temporarily

for (j=0;j < 10;j++)

{

LED_On(target);

pause(100);

LED_Off(target);

pause(100);

}

//reset the first iteration flag

flag = 1;

return 1;

} else

{

//an incorrect switch was hit

//indicate a MISS in the LED

LED_On(8);

//turn the target LED off

LED_Off(target);

//activate the buzzer

Activate_Buzzer();

//reset the first iteration flag

flag = 1;

score_add = 0;

return 1;

}

}

}

return 0;

}

int Get_Last_Score(void)

{

return score_add;

}

void Activate_Buzzer(void)

{

int k;

//pulse the buzzer at the resonance frequency

for (k=0;k<10;k++)

{

PTAD |= BIT6HI;

pause(1);

PTAD &= BIT6LO;

pause(1);

}

//continuously apply a voltage to the buzzer

PTAD |= BIT6HI;

pause(400);

PTAD &= BIT6LO;

}

LED_Controller.h

void LED_On(char index);

void LED_Off(char index);

void Initialize_LEDs(void);

void Clear_LEDs(void);

void Load_Registers(void);

void Pin_LEDs_On(void);

void Pin_LEDs_Off(void);

void Flash_Pin_LEDs(char Num_flashes);

void Light_Num_Tries(char numtries);

void Clear_HitMiss(void);

LED_Controller.c

#include <ME218_C32.h>

#include <timers12.h>

#include <stdio.h>

#include "Utility.h"

#include "LED_Controller.h"

//specify the total number of LED slots

static char Num_LED = 16;

//initialze array of LEDs: 0 is off, 1 is on

static char LED_Array [16];

void Load_Registers(void)

{

int i;

//input the data and pulse the clock to load data

for (i = 1; i <= Num_LED; i ++)

{

//input the current segment of data

if (LED_Array[Num_LED - i] == 0)

PTAD &= BIT3LO;

else

{

PTAD |= BIT3HI;

}

//pulse the clock to load and shift the data

PTAD |= BIT4HI;

PTAD &= BIT4LO;

}

//set the data port back to zero

PTAD &= BIT3LO;

}

void Light_Num_Tries(char numtries)

{

int i;

//light the appropriate number of LEDs that indicate number of tries remaining

for (i=0;i<3;i++)

{

LED_Array[10+i] = 0;

if (numtries >= i+1)

LED_Array[10+i] = 1;

}

Load_Registers();

}

void Clear_LEDs(void)

{

int i;

//clear all elements in the LED array

for (i = 0; i < Num_LED; i ++)

{

LED_Array[i] = 0;

}

//load the data array into the shift register

Load_Registers();

}

void LED_On(char index)

{

//set the array index to high

LED_Array[index] = 1;

//load the data array into the shift register

Load_Registers();

}

void LED_Off(char index)

{

//set the array index to low

LED_Array[index] = 0;

//load the data array into the shift register

Load_Registers();

}

void Pin_LEDs_On(void)

{

char i;

//set all of the bowling pin LEDs to high

for (i=0;i<=7; i++)

{

LED_Array[i] = 1;

}

//load the data array into the shift register

Load_Registers();

}

void Pin_LEDs_Off(void)

{

char i;

//set all of the bowling pin LEDs to low

for (i=0;i<=7; i++)

{

LED_Array[i] = 0;

}

//load the data array into the shift register

Load_Registers();

}

void Flash_Pin_LEDs(char Num_flashes)

{

short i;

//flash all of the pin LEDs the specified number of times

for (i=0 ;i<Num_flashes; i++)

{

Pin_LEDs_On();

pause(200);

Pin_LEDs_Off();

pause(200);

}

}

void Clear_HitMiss(void)

{

//clear the hit and miss LEDs

LED_Array[8] = 0;

LED_Array[9] = 0;

Load_Registers();

}

void Initialize_LEDs(void)

{

//initialize the output ports to be zero

PTAD &= BIT3LO;

PTAD &= BIT4LO;

//make sure all shift register ports are zero

Clear_LEDs();

//light the number of tries

Light_Num_Tries(3);

}

Penny_Sensor.h

void Initialize_PennyInsert(void);

char Penny_Insert(void);

Penny_Sensor.c

#include <ME218_C32.h>

#include <stdio.h>

#include <ADS12.h>

#include "Utility.h"

#include "LED_Controller.h"

#include "Penny_Sensor.h"

void Initialize_PennyInsert(void)

{

//set M5 as penny sensor input

DDRM &= BIT5LO;

}

char Penny_Insert(void)

{

//return 0 to remain on this stage; 1 to move to next stage

static unsigned char prev_state;

unsigned char current_state;

char state_change;

//wait for the start button to be pressed

//get the current state of the penny sensor

current_state = PTM & BIT5HI;

//detect a state change

state_change = State_change(prev_state, current_state);

//set the previous state equal to the current state

prev_state = current_state;

if (state_change == 2)  //if the penny was inserted

{

//flash the pin LEDs to indicate that penny was inserted

Flash_Pin_LEDs(2);

//clear the hit and miss LEDs

Clear_HitMiss();

return 1;

}

return 0;

}

Pre_Start.h

char Get_Difficulty(void);

void Initialize_PreStart(void);

char Start_Press(void);

Pre_Start.c

#include <ME218_C32.h>

#include <stdio.h>

#include <ADS12.h>

#include "Utility.h"

#include "LED_Controller.h"

#include "Timer_Controller.h"

#include "Pre_Start.h"

static char last_diff = 3;

static char uncertainty = 2;

char Get_Difficulty(void)

{

unsigned int ADRead;

//read AD0 (potentiometer)

//132 is the max using 6.XK voltage divider

ADRead = ADS12_ReadADPin(0);

//return the appropriate difficulty level

if (ADRead < 44 - uncertainty)

{

//adjust the timer

Set_Timer(1);

last_diff = 1;

return 1;

}

else if (ADRead >= 44+uncertainty && ADRead < 88-uncertainty)

{

//adjust the timer

Set_Timer(2);

last_diff = 2;

return 2;

}

else if (ADRead >= 88 + uncertainty)

{

//adjust the timer

Set_Timer(3);

last_diff = 3;

return 3;

}

else

{

//we are in between difficulties; leave difficulty the same

Set_Timer(last_diff);

return last_diff;

}

}

void Initialize_PreStart(void)

{

//set M4 as start button input

DDRM &= BIT4LO;

//try to initialize the AD interface

if (ADS12_Init("OOOOOOOA") == ADS12_OK)

{

}

else

{

//the initialization falied

printf("AD Initialization Failure\r\n");

}

//initialize all of the outputs to zero

PTAD &= BIT1LO;

PTAD &= BIT2LO;

PTAD &= BIT3LO;

PTAD &= BIT4LO;

PTAD &= BIT5LO;

PTAD &= BIT6LO;

PTAD &= BIT7LO;

}

char Start_Press(void)

{

//return 0 to remain on this stage; 1 to move to next stage

static unsigned char prev_state;

unsigned char current_state;

char state_change;

//wait for the start button to be pressed

//set the previous state to be low

prev_state = 0;

//get the current state of the start button

current_state = PTM & BIT4HI;

//detect a state change

state_change = State_change(prev_state, current_state);

//set the previous state equal to the current state

prev_state = current_state;

if (state_change == 1)  //if the start button was pressed

{

//flash the pin LEDs to wait for user to get into position

Flash_Pin_LEDs(5);

//set the last difficulty

last_diff = 3;

return 1;

}

return 0;

}

Prize_Dispense.h

void Initialize_Prize(void);

char Prize_Dispense(char numtries, int score);

char Prize_Rotations(int score);

void Clear_Register(void);

Prize_Dispense.c

#include <ME218_C32.h>

#include <stdio.h>

#include "Utility.h"

#include "Prize_Dispense.h"

//specify the number of steps to rotate the stepper motor 90 degrees

static char quarter_rot = 12;

void Clear_Register(void)

{

char j;

//load the data into the shift register

PTAD &= BIT1LO;

//clear the shift register by pulsing low data 9 times

for (j=0;j<9;j++)

{

PTAD |= BIT2HI;

//pause to allow enough pulse width

pause(1);

PTAD &= BIT2LO;

}

}

void Initialize_Prize(void)

{

//initialize the data bit

PTAD &= BIT1LO;

//initialize the clock bit

PTAD &= BIT2LO;

//clear the shift register

Clear_Register();

}

char Prize_Rotations(int score)

{

//determine the appropriate number of 1/4 rotations, depending on //the score

if (score >= 700)

return 3;

else if (score >= 450)

return 2;

else if (score >= 200)

return 1;

else

return 0;

}

char Prize_Dispense(char numtries, int score)

{

int i, j, k;

//determine the number of rotations depending on the score

char prize_rots = Prize_Rotations(score);

//if no tries are left, dispense the prize

if (numtries == 0)

{

for (k=0; k<prize_rots; k++)

{

for (i=0;i<quarter_rot;i++)

{

//load the data into the shift register

PTAD |= BIT1HI;

//pulse clock 4 times for the 4 stepper motor stages

for (j=0;j<4;j++)

{

PTAD |= BIT2HI;

//pause to allow enough pulse width

pause(15);

PTAD &= BIT2LO;

//if this is the first shift, set the data port  back to zero

if (j==0)

{

//set the data port to be low

PTAD &= BIT1LO;

}

}

}

//since 50/4 = 12.5, we need to switch between 12 and 13 //steps every other time to avoid problems

if (quarter_rot == 12)

quarter_rot = 13;

else

quarter_rot = 12;

}

//clear the shift register

Clear_Register();

return 2;

}

else

{

return 1;

}

}

Score_Controller.h

void Pulse_Score(unsigned int pulses);

void Clear_Score(void);

void Initialize_Score(void);

Score_Controller.c

#include <ME218_C32.h>

#include <timers12.h>

#include <stdio.h>

#include "Utility.h"

#include "Score_Controller.h"

void Pulse_Score(unsigned int pulses)

{

int i;

for (i = 0; i < pulses; i ++)

{

//pulse the clock to increment the score

PTM &= BIT1LO;

pause(1);

PTM |= BIT1HI;

}

}

void Clear_Score(void)

{

//send a pulse to the clear bit

PTM |= BIT0HI;

pause(1);

PTM &= BIT0LO;

}

void Initialize_Score(void)

{

//set M0 as clear output

DDRM |= BIT0HI;

//set M1 as clock output

DDRM |= BIT1HI;

//initialize the clock to be zero

PTM |= BIT0HI;

//set the clear output high

PTM &= BIT1LO;

Clear_Score();

Pulse_Score(1);

Clear_Score();

}

Timer_Controller.h

void Set_Timer(unsigned char time_left);

void Clear_Timer(void);

void Initialize_Timer(void);

Timer_Controller.c

#include <ME218_C32.h>

#include <stdio.h>

#include "Utility.h"

#include "Timer_Controller.h"

static unsigned char prev_time = 0;

void Clear_Timer(void)

{

//send a pulse to the clear bit

PTM |= BIT2HI;

pause(1);

PTM &= BIT2LO;

prev_time = 0;

}

void Set_Timer(unsigned char time_left)

{

int i;

//if the time has not changed, exit the function

if (prev_time == time_left)

return;

Clear_Timer();

for (i = 0; i < time_left; i ++)

{

//pulse the clock to increment the timer

PTM &= BIT3LO;

pause(1);

PTM |= BIT3HI;

}

//set the previous time equal to the current time left

prev_time = time_left;

}

void Initialize_Timer(void)

{

//set M2 as clear output

DDRM |= BIT2HI;

//set M3 as clock output

DDRM |= BIT3HI;

//initialize the clock to be high

PTM |= BIT3HI;

//set the clear output low

PTM &= BIT2LO;

//clear the timer

Clear_Timer();

}

Utility.h

void pause(unsigned int miliseconds);

char State_change(unsigned char prev_state, unsigned char current_state);

Utility.c

#include <timers12.h>

#include <stdio.h>

#include "Utility.h"

void pause(unsigned int miliseconds)

{

unsigned int x = TMRS12_GetTime();

//pause until the appropriate time has been reached

while((TMRS12_GetTime()-x) < miliseconds)

{

}

}

char State_change(unsigned char prev_state, unsigned char current_state)

{

//return 1 if we had a rising edge; 2 if we had a falling edge;

//0 if the state remained the same

if (prev_state ==0 && current_state != 0)

{

return 1;

}

else if (prev_state !=0 && current_state == 0)

{

return 2;

}

else

{

return 0;

}

}